## Slide 1: Synthesis of Propionic acid from Syngas
Date:05 April 2011
Team Echo:
Sabah Basrawi
Alex Guerrero
Mrunal Patel
Kevin Thompson
Client Mentor: Shannon Brown

## Slide 2: Presentation Layout
Design Basis
Motivation
Process Flow Diagram
Plant Layout
Economics

## Slide 3: Design Basis
Production of:
  Propionic Acid
  33,000 ton/year
  Using syngas
Synthesized from
    Syngas (1:1 ratio of CO & H2)
    Ethylene
    Oxygen
Notes: Location of Plant:
  Morris, IL
  Near:
    Lyondellbasell (for Ethylene)
    Team Foxtrot (for Syngas)
Google image of land to come in plant layout
The goal of this project is to take the syngas from group Foxtrot, and utilize it for the production of Propionic Acid to be used in industrial processes.
The syngas feed will be reacted with Ethylene to produce Propionaldehyde.
This aldehyde will then be oxidized to become Propionic Acid.
We have decided to base our plant operations in Morris, IL
  Close to Lyondellbasell Plant which produces ethylene.
  **Also near rail line so team Foxtrot can obtain Illinois Basin #6 coal from southern Illinois.

## Slide 4: Chemical Information Analysis
Reaction Mechanism
  Syngas feed with Ethylene  Propionaldehyde
    Catalyst: Rhodium
    (1) CO + H2 +C2H4  CH3CH2CHO
  Aldehyde oxidation  Propionic Acid
    Catalyst: Cobalt Ion
    (2) CH3CH2CHO + ½ O2  CH3CH2COOH
In = Out (per year)
  6.64E7 lb (CO+H2+C2H4+O2)= 6.64E7 lb Product

## Slide 5: Motivation
Increasing demand
Increasing price (price already high)
Easy to synthesize
Wide variety of uses

## Slide 6: Uses of Propionic Acid
Mold inhibitor for various animal feed
Preservative in cheeses and baked goods to prevent mold
Precursor in many industrial processes
  Pharmaceuticals
  Plastics
  Plasticizers
  Textile and rubber auxiliaries

## Slide 7: Block Flow Diagram
Notes: Add flowrates on diagram
Explain the process, there exist three major phases  2 reactions, and product purification

## Slide 8: Process Flow Diagram

## Slide 9: Process Flow Diagram

## Slide 10: Plant Layout
Notes: Google image of land in which the foxtrot and echo plants will be built

## Slide 11: Plant Layout
Notes: Outside view of plant, Foxtrot and transportation adjacent

## Slide 12: Process Floor Plan

## Slide 13: Process Floor Plan

## Slide 14: 3-D
Please enjoy this three dimensional representation of our process

## Slide 15: Competing Processes
Industry standard:
  Hydrocarboxylation of ethylene using nickel carbonyl or ruthenium as catalyst:
    H2C=CH2 + H2O + CO → CH3CH2COOH
Our process :
  Hydroformylation involves the addition of a formyl group (CHO) and a hydrogen atom to a carbon-carbon double bond.
  Promotes chain extension
Notes: Competition for feed stock, who else wants this feed stock?
Availability of source, source depletion
Why this source as opposed to another source
Variations in fischer-tropsch technology
Methanol homologation to ethanol, followed by hydration
Dimethyl ether cracking
Direct synthesis from CO/H2 mixtures over alkaline iron oxide catalysts
Billion ton vision, first bullet point

## Slide 16: Competing Processes Pt. 2
Choice of Syngas:
  The feed for the process since it’s thermodynamically efficient
Wacker process:
  Similar to Hydroformylation
  uses a Tetrachloropalladate catalyst.
Carbonylation Process:
  Produces Propionaldehyde, then oxidizes it in the presence of cobalt ions to produce Propionic Acid.
  Typically requires a carbonyl catalyst like Nickel Carbonyl
Notes: http://en.wikipedia.org/wiki/Propanoic_acid
Ethylene formation and propanoate
Rh vs Pd vs NiCO

## Slide 17: Economics
NPV: -$20 Million
IRR: 4%
Capital Cost: $57.8 million
Total Yearly Cost: $28.6 Million
Total Yearly Profit: $28.8 Million
Break-Even Point: ~18.5 Years
Notes: Interest 8%
Arbys and Taco bell use propionic acid
Farmers use propionic acid
Plans to have 40 workers across four differing shifts
Plans for plant to be operated 337 days per year
Plans to sell propionic acid to food companies

## Slide 18: Reccomendations
Move the project forward if
  Increase syngas H2 Ratio
  Find alternate H2
  Increase Propionaldehyde selectivity
Otherwise, do not proceed

## Slide 19: Contact Information
Wiki link: http://seniorecho.wikispaces.com/
Email: designecho@listserv.uic.edu

## Slide 20: References
"Acetic Acid Production." Acetic Acid Production. 2009. Web. 22 Jan. 2011. <http://www.starcontrols.com/Application/Application_min_e.asp?MinID=34>.
Boyaval, P., and C. Corre. Production of Propionic Acid. 1995. Print.
Perlack, Robert D., Lynn L. Wright, Robin L. Graham, Bryce J. Stokes, and Donald C. Erbach. Biomass as a Feedstock for a Bioenergy and Bioproducts Industry: The Technical Feasibility of a Billion-Ton Annual Supply. Print.
"Propanoic Acid." Wikipedia, the Free Encyclopedia. Web. 22 Jan. 2011. <http://en.wikipedia.org/wiki/Propanoic_acid>.
Registration Review Document for Propionic Acid and Salts. Mar. 2008. Print.
Spivey, James J., Makarand R. Gogate, Ben W. Jang, Eric D. Middlemas, Joseph R. Zoeller, Gerald N. Choi, and Samuel S. Tam. Synthesis of Acrylates and Methacrylates from Coal-Derived Syngas. 1997. Print.

## Slide 21: References Pt. 2
http://www.engineeringtoolbox.com/air-compressor-types-d_441.html

## Slide 22: QUESTIONS

## Slide 23: Flowsheeting
Notes: Overall flowsheet, will be done in parts in the next few slides for readability

## Slide 24: Flowsheet (Left Side)
Notes: Reaction1: Production of Propionate from Syngas

## Slide 25: Flowsheet (Center)
Notes: Reaction 2: Production of Propionic acid from Propionate

## Slide 26: Flowsheet (Right Side)
Notes: Purification of Propionic Acid to meet industrial standards

## Slide 27: In=Out
IN | Mass/ Year | Out | Mass/year
CO | 2.5 E07 lb | Propionic Acid | 3.20E07 lb
H2 | 1.9 E06 lb | Ethane | 1.29E07 lb
C2H4 | 2.5 E07 lb | CO | 1.22E07 lb
O2 | 7.2E06 lb |  | 

## Slide 28: Salaries and Fringes

## Slide 29: Capital Cost Sensitivity
Chart: Capital Cost Sensitivity
| 8.7238288279495493E-2 | 6.8466689897023494E-2 | 5.7022590364616439E-2 | 4.9138674667461267E-2 | 4.2316621544319845E-2 | 3.8791111261782342E-2 | 3.5171831433620925E-2 | 3.2198349331199458E-2 | 2.9706832549508379E-2
 | 20 | 30 | 40 | 50 | 62 | 70 | 80 | 90 | 100

## Slide 30: Syngas Sensitivity
Chart: Syngas Price Sensitivity
| 9.6544613739501503E-2 | 8.449927491854678E-2 | 7.1934310764202716E-2 | 5.8674059667816678E-2 | 4.4459539890528442E-2 | 2.8886609059614602E-2 | 1.1272447870484268E-2 | 0 | 0 | 0
 | 1000000 | 2000000 | 3000000 | 4000000 | 5000000 | 6000000 | 7000000 | 8000000 | 9000000 | 10000000

## Slide 31: Propionic Acid Price Sensistivity
Chart: Product Price Sensitivity
| 0 | 0 | 0 | -2.1982831874897682E-3 | 4.4459539890528456E-2 | 8.0376080219517199E-2 | 0.11200647607461978 | 0.14157214324363537 | 0.17007434598230833 | 0.19802157416382987
 | 1400 | 1500 | 1600 | 1700 | 1800 | 1900 | 2000 | 2100 | 2200 | 2300